## Slide 1: ATLAS Upgrade
Jornadas do LIP
Universidade de Coimbra – 8 July 2022
Ricardo Gonçalo
Universidade de Coimbra / LIP
Notes: Agradecer o interesse!
E aos alunos por tirarem uma hora para me ouvir falar sobre coisas de que gosto

## Slide 2: ATLAS Upgrade: Motivation for HL-LHC
High-Luminosity!
  Statistical uncertainty depends on √L
So far collected ≈150 fb-1 of data at √s=7, 8 and 13 TeV
  Less than 5% of final
  Resulted in 1039 published papers
  Goal is to collect up to 4000 fb-1 until end of LHC
=> Increase instantaneous luminosity!
Downside: PILEUP
  Affects experiment performance
  Average ≈30 so far
  Expect up to 200 in HL-LHC
Notes: Statistical precision depends on sqrt(L)

## Slide 3: ATLAS Upgrade: pileup = 200

## Slide 4: ATLAS Upgrade @ LIP
High Granularity Timing Detector
(30ps/track)
Track reconstruction for New Inner Tracker (ITk)
New Tile Calorimeter High-Voltage system
R&D on hardware acceleration for trigger

## Slide 5: ATLAS TileCal Upgrade
HV System: Agostinho Gomes, Guiomar Evans, Luís Gurriana, Filipe Martins, José Augusto, Rui Fernandez, Pedro Assis, Miguel Ferreira, José Carlos Nogueira (collaboration with eCRLab)
Optics Robustness: Rute Pedro, Beatriz Pereira

## Slide 6: TileCal High-Voltage System
HVRemote boards - Regulation and control system off detector at USA15 (256 boards)
16 crates in service cavern
>100m long cables
from service cavern
System parameters:
10000 PMTs
High Voltage < 950 V – so far used ≈750 V
Individual currents < 400 mA
High Voltage stability < 0.5 V rms
HVBus – passive distribution board distributes HV to PMTs (1024 boards)
DCS system: SoC board for High Voltage monitoring & control
HVSupplies provide primary High Voltage
(256 boards)

## Slide 7: High Voltage System Components
Front of crate: HVSupplies board
Back of crate: HVRemote boards
Middle plane

## Slide 8: High Voltage System Components
HVSupplies:
DC-DC converters to produce primary HV
Connects with the ATLAS Detector Safety System Designed by eCRLab
First prototypes successfully tested and a new design finished for production
HVRemote:
Receives 2 primary HV inputs from HVSupplies
Sends 48 individually regulated HV outputs to HVBus
  DACs to set the individual voltages
  Regulation loops based on optocouplers
  On/Off available for sets of 4 channels
HV Control Board:
One Zybo Z7 Zynq System-on-Chip (SoC) interface board per crate
Two SPI buses (one to the HVRemote and other to the power supply boards);
Tests showed a few bugs, some corrections required

## Slide 9: High Voltage Distribution
Cables:
New 48 wire pairs cable developed in Portugal with General Cable
  10000 PMTs => 20000 wires 100 m long
  > 41 km for final system
  Wire diameter: 0.4 mm
  Aluminium/PETP tape screen and drain wire ensures electromagnetic shielding
  Prototypes produced
HVBus:
HV bus and short cables for HV distribution produced and being tested

## Slide 10: Testing Programme
Testbeam:
  Tested HVSupplies + adapter board + HVRemote + Hvbus in 2021 and June 2022
  Will test Crate + SoC interface + final boards in November 2022
Stability tests:
  > 5h long tests
  rms ≈ 0.21 – 0.23 V
Chart: 

## Slide 11: TileCal Optics Robustness for HL-LHC
The HL-LHC will bring additional radiation exposure and damage to the TileCal scintillators and fibres
Measured Run 2 light yield from Laser and Cs data
Modeling the light response as a function of ionising dose
Cs calibration data at sub-cell level helps to reduce uncertainties due to dose spread within the cell volume (ongoing work)

## Slide 12: High Granularity Timing Detector
HV System: Luis Lopes, Orlando Cunha, Ricardo Gonçalo – collaboration with Detector Lab
ASIC tests: Rui Fernandez, Pedro Assis, Miguel Ferreira – collaboration with eCRLab
DCS and Interlocks: Filipe Martins, Rui Fernandez, Helena Santos, Guiomar Evans

## Slide 13: HGTD @ LIP
Recent involvement since last year, but significant impact
Contributing to several areas:
  Electronics: readout ASIC tests, High Voltage filtering
  Detector control and safety Interlocks
  Monitoring
Other possibilities being followed:
  Cable production in Portuguese industry
  Mechanical design and production at LIP

## Slide 14: Electronics and High-Voltage
HV patch panels:
Responsible for producing HV patch panels
Routing and filtering High Voltage to HGTD detector
Preliminary layout done and prototype tested
Design being updated after review
Cables:
May also produce HV cables (under negotiation)
ALTIROC:
ASIC under development for LGAD readout
Plan to take part in ASIC development tests
Contact established with developers (OMEGA) and testing infrastructure almost in place
Chart: 
| 0.0 | 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.176091259055681 | 3.301029995663979 | 3.397940008672037 | 3.477121254719662 | 3.69897000433602 | 3.8750612633917 | 4.0 | 5.0 | 5.698970004336015 | 6.0
Shielding; direct; 33 nF | 0 | -0.33199 | -2.4988 | -7.2803 | -13.4324 | -18.0444 | -21.5403 | -27.5869 | -32.0412 | -36.1934 | -38.2373 | -46.4661 | -56.4782 | -58.0618 | -58.0618 | -58.0618 | -58.0618 | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
Shielding; direct; 47 nF | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
No shielding; direct; 33 nF | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206 | -46.0206 | -46.0206 | -46.0206

## Slide 15: DCS and Interlocks
Detector Control System (DCS):
  Contributing to DCS architecture definition
  Readout of DCS environment data through ELMB2 communication board
Interlocks (started recetly):
  Taking responsability for HGTD Interlocks – mostly will re-use ITk design
    Likely to produce an interlock module ourselves (HV-Present)

## Slide 16: Reconstruction Algorithms for Phase 2
GPUs: Nuno Fernandes, Patricia Conde
Muon trigger: João Gentil
ACTS: Luis Coelho, Noemi Calace, R.goncalo

## Slide 17: ATLAS Trigger Upgrades
GPU acceleration to deal with increased event rates
  GPU-based Topo-Automaton Clustering (TAC) cellular automaton algorithm
    Group cells by signal-to-noise ratio
    Important overhead from data structure convertion to and from GPU format
Speed-up:
  3.5 (di-jets) to 4.5 (top pairs)
  < 40% of time: algorithm
  50 - 55% of time conversion overhead
  10 - 15% of time CPU↔GPU data transfer (TeslaT4andaAMDEPYC7552)
Also new Muon trigger:
  Using minimum-bias scintillators for fake jet rejection (J.Gentil)

## Slide 18: A Common Tracking Software (ACTS)
Tracking of charged particles is one of the the most complex and CPU consuming phases of event reconstruction
Will become even greater computational challenge during HL-LHC
ACTS:
Experiment-independent toolkit for particle track reconstruction
Designed for modern computing architectures and multi-threaded event processing
Goal:
Implement ITk seeding algorithm in ACTS and integrate into standard ATLAS code and validate its performance
The Seeding Algorithm
Forms track seeds consisting of triplets of space-points (SP) based on geometrical assumptions relative to the interaction point

## Slide 19: Summary and Outlook
A lot of activity was started on upgrades for HL-LHC since the last LIP Jornadas
Interesting times!
  First HL-LHC run will be on 2029 – 7 years to develop, build, install,and commission – Lots of fun ahead!

## Slide 20
E-mail: Ricardo Gonçalo (jgoncalo@lip.pp
Backup Slides