## Slide 1: Investigação na Experiência ATLAS

## Slide 2
Mont Blanc
ATLAS
Notes: LHC Running at 2x design luminosity
Expect 150/pb by end of this year

## Slide 3
Notes: Th only experiment I know with its own super-hero!

## Slide 4
Notes: 3000 physicists and engineers including 1000 postgraduate students

## Slide 5
Solenoid: B = 2 T
Inner Tracker: || < 2.5
Si pixels/strips and Trans. Rad. Det.
/pT = 0.05% pT (GeV)  1%
Muon Spectrometer: || < 2.7
Air-core toroid + gas-based muon chambers
σ/pT = 2% @ 50GeV to 10% @ 1TeV (ID+MS)
EM calorimeter: || < 2.5 (3.2)
Pb-LAr accordion sampling
/E = 10%/E  0.7%
Hadronic calorimeter:
Fe/scintillator / Cu/W-LAr
/Ejet= 50%/E  3%
L = 44 m,  ≈ 25 m
7000 tonnes
≈108 electronic channels
2-level trigger reducing 40 MHz collision rate to 1 kHz of events to tape
Notes: Parts of the experiment  LIP contributed to the TileCal

## Slide 6
Notes: LIP made an important contribution to the TileCal

## Slide 7
Etapas do projecto Tilecal (1993-2009)
2004-2006 Instalação
1993-1995 R&D-protótipos
1999-2002 Instrumentação
1996-2002:construção
1999-2004: Electrónica
2002-2004: calibrações
2007-2009 certificação
(raios cósmicos)
2009--: aquisição/análise dados LHC
Notes: Phases of the project

## Slide 8
Notes: Wavelength fibres which take light from scintillators to PMTs and adapt wavelength  made at LIP
Quality control instrument: fibres tested at LIP
One Tile module

## Slide 9
USA15
SDX1
Gigabit Ethernet
Event data requests
Delete commands
Requested event data
Regions Of Interest
LVL2
Super-
visor
Network switches
Second-
level
trigger
pROS
~ 500
stores
LVL2
output
LVL2
farm
UX15
Read-
Out
Drivers
(RODs)
First-
level
trigger
Dedicated links
VME
Data of events accepted
by first-level trigger
Read-Out
Subsystems
(ROSs)
USA15
1600
Read-
Out
Links
RoI
Builder
~150
PCs
Event data pushed @ ≤ 100 kHz,
1600 fragments of ~ 1 kByte each
Timing Trigger Control (TTC)
DataFlow
Manager
Event
Filter
(EF)
~1600
Network
switches
Event data
pulled:
partial events
@ ≤ 100 kHz,
full events
@ ~ 3 kHz
SDX1
dual-CPU nodes
CERN
computer
centre
Event rate
~ 200 Hz
Data
storage
6
Local
Storage
SubFarm
Outputs
(SFOs)
~100
Event
Builder
SubFarm
Inputs
(SFIs)
Trigger / DAQ architecture
Notes: Other important contribution over last 10 years: trigger

## Slide 10
Notes: Main area: jet trigger
GPU-based clustering for the upgrade

## Slide 11
New tracking detector
Calorimeter: new DAQ electronics, HV sources and gap scintillators
New dedicated hardware tracking co-processor for trigger
New muon detector “Small Wheel”
High Granualrity Timing Detector
(30ps/track)
R. Gonçalo - LIP
Ciência 2018
11
Notes: UPGRADE: (LIP areas in red)
Add spacial granularity to separate close tracks and add tracking solid angle (b-tagging, vertex ident. Etc)
Add timing information to reject pileup: need O(mm) resolution => ~O(10ps) ; 30ps = 9mm
Replace damaged detectors with more rad.hard technologies
HGTD radius 120 – 640 mm ;  Completely replace Inner Detector with all-silicon

## Slide 12: The Run 1 legacy
Notes: Now Higgs physics: the discovery announced to the world
Helena will talk about Heavy Ions next

## Slide 13: Higgs decay to b-quarks
9 July 2018
Notes: VH channel with H bb observed last year after many years searching  one of LIP’s involvements

## Slide 14
Higgs production with top quarks
Notes: The other Higgs area at LIP: ttH observed last year
http://atlas.web.cern.ch/Atlas/GROUPS/PHYSICS/PAPERS/HIGG-2018-13/
data event from the tt̄H(γγ) Had BDT bin with the largest signal over background ratio. The event contains two photon candidates, with a diphoton mass of 125.4 GeV. In addition, six jets are reconstructed using the anti-kt algorithm and R=0.4, including one jet that is b-tagged using a 77% efficiency working point. The photons correspond to the green towers in the electromagnetic calorimeter, while the jets (b-jets) are shown as yellow (blue) cones.

## Slide 15: Probing the 125 GeV Higgs
BSM
Triple coupling λ3
2HDM
Yukawa
couplings
Ribs
Aorta
Clavicle
Notes: Now they can be used as tools to probe the Higgs

## Slide 16
Phys. Rev. D 96, 013004 (2017)
Notes: Example for the near future: find if CP quantum numbers hold surprise  using a method proposed by us

## Slide 17: https://www.lip.pt/atlas/ atlasinfo@lip.pt
Notes: More info at...