## Slide 1: ATLAS Upgrade: HGTD

## Slide 2
HTT electronics and software
        Hardware tracking co-processor for the trigger:
          Abandoned by ATLAS in favour of a solution based on software+commodity hardware
        Contributions from LIP:
          HTT fast simulation; studies of tracking performance – PHD Qualif. Task
          Alternative tracking algorithm (Hough transform) – MSc thesis
          Development of TP network interface – only started; TP prototype received late
          Didn’t get here: production of RTM board and DCS
          Team: 1 academic, 2 engineers, 1 PhD student, 1 MSc student

## Slide 3
High Granularity Timing Detector
        Two detector wheels at ±3.5 m from IP
        7 m2 area, covering region of 2.4<||<4
        8032 LGAD modules of 20×20 mm2
        Pixel pitch of 1.3×1.3mm2
        Time resolution 30 – 50 ps / track
        Aims to improve pileup rejection and luminosity measurement

## Slide 4: HGTD High Voltage Patch Panels
Aim was developing HV patch panels for CERN group:
16 patch panel boxes located around the calorimeter
  Routing of High Voltage to HGTD detector and filtering out AC noise
Collaborating with Detector Lab. (Coimbra)
  Luis Lopes; Orlando Cunha
  Proposed design and presented in Electronics meetings
  Built and tested prototype
Now contributing to Specifications Review (SPR) document
Proposal to HGTD: produce patch panels ourselves at LIP as in-kind contribution – 85 kEUR
Notes: Possibilities: TDAQ and DCS

## Slide 5
Detector Control System
        HGTD DCS design
          Filipe Martins contributed to DCS Specifications Review
          Helena interested in taking part – tbd how
          Filipe working on alternative data transfer scheme following panel recommendations – data path separate from FELIX
        FELIX firmware in collaboration with eCRLab:
          Part of DCS data to be transferred through FELIX
          Rui Fernandez to start contributing to firmware
          Next steps depend on investigation by Filipe and on system decision – alternative means possible MoU contribution
        Proposal to HGTD: involvement in HV DCS with person power

## Slide 7
Altiroc ASIC
        Getting involved with testing Altiroc v.2
          In collaboration with eCRLab
          6 institutes already involved – but interest in gaining experience with this
          Rui Fernandez involved, with support from Miguel Ferreira and Pedro Assis
        In contact with Omega lab. to obtain material, to install a test setup at LIP
        Proposal to HGTD: involvement in Atiroc development with person power (little cost)

## Slide 8: Impact and Upgrade MoU
HTT: MoU share of ~600 kEUR
HGTD project:
Only ~112 kEUR CORE funds missing, in HGTD DAQ (some 6 months ago)
Little existing experience in DCS – possible important impact from group
Developing challenging Altiroc front-end ASIC – technological interest
Patch panels – way into project and possible group responsability – 85 kEUR
Ideal: pay people from MoU – maybe easier on TDAQ tasks
Other areas:
Interlocks:
  Mostly temperature sensors connected to Interlock Matrix Crate (IMC) located in USA15, similarly to Itk
  Possible LIP involvement: interface to ATLAS interlock system (15 kEUR)
Performance studies:
  Suitable for student qualification tasks

## Slide 9
Thanks!
Acknowledgments

## Slide 10: Possible areas of involvement
DCS:
Software involvement – much expertise in the group
Interlocks:
Mostly temperature sensors connected to Interlock Matrix Crate (IMC) located in USA15, similarly to ITk
DAQ, Lumi, timing?:
Firmware (& hardware?) – opportunity for collaboration with eCRLab and João Varela/CMS
Performance studies:
Suitable for student qualification tasks
112 kCHF CORE funds missing (TDAQ)

## Slide 11
Backup