## Slide 1: High Granularity Timing Detector
Ricardo Gonçalo (U. Coimbra, LIP)
on behalf of the HGTD Group
ATLAS Week, Lisbon, October 2022

## Slide 2: The High Granularity Timing Detector
Two detector wheels between ITk and endcap:
  z = ±3.5 m; 7.5 cm thick (+5 cm neutron moderator)
  Active detector region: 2.4 < |η| < 4.0
  8032 modules with 2 hybrids each (sensor + readout ASIC)
  3.6 M channels; 1.3×1.3 mm2 pixels; 6.4 m2 active area
  Radiation hardness: up to 2.5x1015 Neq /cm2, 2 MGy
Pileup rejection:
  Identify track vertex in forward region (poor ITk zVTX resolution)
  30-50 ps/track, 35-70 ps/hit resolution
Luminosity measurement:
  Count number of hits at 40 MHz to get bunch-by-bunch luminosity
  Goal is 1% luminosity uncertainty

## Slide 3
Low Gain Avalanche Detector (LGAD) sensors:
Mounted on both sides of cooling disks
Active region: 12 cm < r < 64 cm
Peripheral electronics: 64 cm < r < 100 cm
Three regions with different sensor overlap
Neutron moderator (5cm) to shield detector from backscattered neutrons
HGTD Modules:
LGADs bump-bonded to two ALTIROC ASICs: 2×2 cm2
15×15 pads of 1.3×1.3 mm2
Operated at -30 °C (CO2 cooling) to cope with radiation damage
Internal moderator
Outer ring and CO2 lines
External moderator

## Slide 4: Low Gain Avalanche Detector Sensors
Aim for 70 ps/hit timing resolution after full irradiation
Thin ≈50 μm active layer on thick ≈300 μm substrate
Multiplication layer
  Affected by irradiation originated defects (acceptor removal)
  Compensated by higher bias voltage up to a point
Single Event Burnout (SEB) in irradiated sensors at high HV
  Above 12 V/μm or ≈600 V/50 μm wafers
Robustness improved by carbon-enriched gain layer
  Only carbon-enriched gain layer modules viable for operation

## Slide 5
Testing sensors from 4 different vendors – with carbon-enriched gain layer
Test program for sensors and sensor+ALTIROC assemblies
Sensors from at least 3 vendors satisfy the requirements to be used in HGTD
Tendering process in preparation
  Expect contracts awarded in December – 1.5 month delay
  Will accelerate procedure and stagger production to avoid delays

## Slide 6: ALTIROC frontend ASIC
Readout of 15×15 LGAD pixels
2×2 cm2 bump-bonded to sensors
Specifications:
  Jitter < 25ps @ 10 fC; <65ps @ 4 fC
  Minimum threshold: 2 fC
Outputs:
  Time Of Arrival (TOA)
  Time Over Threshold (TOT)
  Luminosity (No. of pixels hit)
ALTIROC 2: first full size prototype; tests being finalized at several institutes
ALTIROC 3: to be submitted in November

## Slide 7
Intensive ALTIROC 2 testing program:
ASIC alone found to be close to specifications
But additional noise found in ASIC + LGAD sensor assembly
  Due to parasitic inductances separating sensor/preamp grounds
  Effect amplified due to 10 nF HV decoupling capacitor
  Removing capacitor gave lower noise and so Qmin = 2.6 fC instead of 4 fC with capacitor
Qmin = 2.6 fC
Removing 10 nF capacitor

## Slide 8: ALTIROC 3
Improvements with respect to ALTIROC 2:
  Identified bottleneck for trigger rates > 1 MHz giving high FIFO occupancy
  Modifications for smaller Qmin and jitter to address:
  Voltage drops between grounds solved in ALTIROC 3
  Digital noise injected through preamplifier ground
  Higher redundancy to improve robustness against Single Event Effects
  40 MHz clocks in ALTIROC 3 matrix de-skewed along the columns and between columns to avoid high digital current spikes
Power consumption slightly higher : 1.4 mW/ch vs 1.2 mW/ch
  ALTIROC plans: PDR set to October 18
  Design of ALTIROC 3 version is now ready – verifications in coming month
  Submit to foundry in early November – to arrive at CERN early Feb. 2023
HGTD-ALTIROC-A – pre-production ASIC
  Design to start in April 2023 and FDR in October 2023

## Slide 9: HGTD Modules
Hybridization: Sensor bump-bonded to ASIC
  Technique established at several sites
  Detailed tests (shear test, X-ray examination) have shown good bonding results achieved
  Beam tests at CERN in July and September; next one in 19/10 – 02/11
Five full modules produced and more without sensor
  Load to be spread between several institutes
Dedicated tools developed:
  Bending the flex, aligning and placing the bare module on the flex, and glueing the assembly
Support units developed and prototypes tested

## Slide 10: Peripheral Electronics Boards
Prototype (PEB 1F) design to finish soon – some delays to understand communication with FELIX and to simplify PEB design, to save time/complexity later on:
  Space limitations on rigid PCB for connectors and components required flex tails integrated into rigid PCB
  A lot of individual testing of components (lpGBT, VTRX+) already done
PDR in Nov 2022; PEB 1F Production: Dec 2022-Jan 2023
Modular PEB
Timing lpGBT
Lumi lpGBT
Module emulators
To FELIX
Flex tails
PEBs

## Slide 11: And Much Much More!...
Heater and DAQ demonstrators
And a mockup for cable routing
Test beams and sensor irradiation
Full update of mechanics vessel design, ready for PDR
DCS and Interlocks development
Grounding and shielding
Beamtest paper accepted: link
Etc, etc...

## Slide 12: Project Overview
LGAD Sensor production: Tendering ongoing
Pre-production to start in December, followed by tests
ALTIROC ASIC: Critical, FDR October 2023
ALTIROC3 to be submitted early November
Pre-production (ALTIROC A) design starts April 2023
Peripheral electronics boards: PDR (PEB 1F) November 2022
Complex large boards with 6 versions – design slightly behind
Design of other versions to start in January 2023
HV Power Supplies: PDR passed in September 2022
Ordering full-size prototypes for evaluation
PDR raised questions on gounding scheme (single-point vs mesh)
LV Power Supplies: FDR planned for December 2022
Pre-production expected in March 2023
Modules, Flex cables, Detector units: PDR planned for Dec 2022
Production of 50 modules for full demonstrator by February 2023
Mechanics and on-detector cooling: PDR in November 2022
Services, CO2 cooling, N2, Cables, Fibres: PDR in November 2022
Lost around 2 months due to delay in ASIC submission
But delays now stabilized – only 1 week lost in last quarter
Project contingency:
HGTD-A: 238 working days
HGTD-C: 151 working days

## Slide 13: Thanks for listening!