## Slide 1: Single-beam chains

## Slide 2: Single-beam chains
Being setup in TriggerMenuPython (Rasmus):
  In SingleBeam_v1.py and SingleBeam_v2.py
  First phase (SingleBeam_v1.py):
    MBTS commissioning with 32 L1 items + MBTS_A/MBTS_C
    HLT: taus more or less complete; rest incomplete
  Second phase (SingleBeam_v2.py):
    Only L1 so far
Would like to have L2 and EF algorithms with minimal changes:
  No c++ changes if possible
  Loose tunings (parameters) of FEX and hypos
So far:
  Loose chains planned from each slice (slice contributions later)
  Chains starting from MBTS/something else:
  T2CaloEgamma:
    Start from MBTS_A or MBTS_C and open wide ROIs
    Add a Hypo algo after T2Calo with very loose cuts
  TrigEgammaRec:
    EF AllTeAlgo to do unseeded full-calorimeter reconstruction (Phillip)
  Currently no tracking for either L2 or EF: to be added

## Slide 4: T2CaloEgamma from MBTS
Tested online (Denis and Alex)
  NAV_ERROR returned by algo when no TrigEMClusters produced
  All events sent to debug stream
  Needs minor fix to algo (would always be necessary)
  Taken out of the menu; Alex working to re-integrate it
Points to necessity of testing new chains online asap

## Slide 5: L2 muon full scan
Plan to use a chain modified from mu4_dimu_fs
Starts from L1_MU4
HLT chain counter 390
  L2_MU4_DiMu_FS
  EF_MU4_DiMu_FS
Uses TrigDiMuonFast at L2
Plan to use existing L2 setup in new chain
A muon trigger from the endcap is possible (see talk by Masaya) in the last Core & Slices meeting http://indico.cern.ch/conferenceDisplay.py?confId=24854

## Slide 6: Plans
This week expect to have T2Calo running from MBTS
Add tracking (full scan)
Add full-scan muon chain from L1 endcap item
Anything else?