## Slide 1: HGTD Patch/Filter Panels
Luis Lopes, Orlando Cunha, Ricardo Gonçalo
LIP - Portugal

## Slide 2: First CAD drawings
Only a general scheme so far, but ready to move to prototyping and testing as soon as parts are agreed on
Next steps:
  Decide on parts:
    Connectors: used 56-pin CMM 320 series from Nikomatic (from initial discussion with Sergei)
    SMD R and C components: need specs to procure
  Acquire components for a small prototype
  Assemble test boards and perform electrical tests

## Slide 3: Modular box
Dimensions: 360 x 195 x 104 mm3 Weight: 7.5 kg (final around 10 kg)
56 wires in (28 pairs)
For insulation: male pins on USA15 side; female plugs on sensor side

## Slide 4: Filter module
Mechanically independent and insulated modules

## Slide 5: Filter module
Two PCBs per module with filters

## Slide 6: PCB with filters
14 RC-RC filters per PCB – 28 per module / Wire routing from connector to filter
Patching options:
56 wires in (28 pairs) – 56 wires out (28 pairs)
48 wires in (24 pairs) – 56 wires out (28 pairs)

## Slide 7: Backup

## Slide 8: Outlook
LIP interested in producing HV patch/filter panels
First meeting with Bengt Lund-Jensen, Sergey Malykov, Ana Henriques, João Guimarães (thanks!)
First idea now formed, but we need more information to continue

## Slide 10: Current understanding
Originally: patch panels map 11 cables (x48 wires) to 10 cables and filter HV
BUT current thinking is: filter boxes near detector and separate HV patch panels in USA15
  Probably easier design and better accessibility to each channel
Filter boxes:
  16 boxes / endcap
  In & out: 10/11 cables of 24 pairs (48 wires) each
  Means 240/264 filters / box
  Low-pass filters (RC-RC)
From Sergey’s slides

## Slide 11: Requirements:
Magnetic field: must withstand 0.5 T
Activation: use Aluminium and avoid steel
  Grounding:
    Floating cable pairs – not connected to box (Faraday cage)
    Cable shielding connects to power supplyfloating shield, not filter box
    Grounding scheme in Bengt’s talk 2 weeks ago

## Slide 12
Simplest solution for filter boxes
1 cable in / 1 cable out (48 pairs/cable)
Assuming RC-RC filter with discrete SMD components
24 channels / board
Can use both sides of each board if needed

## Slide 13
Identified possible connector:
52 HV pins
Insulator : Thermoplastic UL94V0 - halogen free and rad.hard
Backshell & shroud : Aluminium alloy nickel plated
Locking device : Stainless steel and nickel plated copper alloy
  Can probably be replaced
Contacts : Copper alloy gold over nickel plated.
Notes:
Already used in ATLAS & etc
Expensive?
19mm wide plus margin should be easy for 10/11 in 40cm box – anything we’re missing?

## Slide 14: Questions:
Need more information to proceed:
Is this design suitable or do we need other options?
Filter characteristics?
  Identified range of SMD components but need to know values of capacitance and resistance
  What power / current per channel?
  Is there a list of allowed materials / components?
  Any limits on cross-talk between channels?
  Accessibility and ease of maintenance:
    In case of failure assume whole box is taken to repair? Or best to access individual boards?
Anything else we’re missing?
Once the above are understood we can make proper design and start testing
  Would be very useful to decide which connector will be used
  Would it be possible to obtain one LGAD of the type we’ll use?