## Slide 1: HGTD Patch/Filter Panels
Luis Lopes, Orlando Cunha, Ricardo Gonçalo
LIP - Portugal

## Slide 2
16 Patch Panel boxes
Routing of HV channels from sources to detector
Filtering AC noise
Proposed design shown in next few slides

## Slide 3: Modular box
Dimensions: 360 x 195 x 104 mm3 Weight: 7.5 kg (final around 10 kg)
56 wires in (28 pairs)
For insulation: male pins on USA15 side; female plugs on sensor side

## Slide 4: PCB with filters
14 RC-RC filters per PCB – 28 per module / Wire routing from connector to filter
Patching options:
56 wires in (28 pairs) – 56 wires out (28 pairs)
48 wires in (24 pairs) – 56 wires out (28 pairs)

## Slide 5: Filter module
Initial idea: two PCBs per module with filters

## Slide 6: Filter module
Mechanically independent and insulated modules

## Slide 7: Status of development
Preparing to build initial “Prototype 0”
Will produce 2 equipped boards for basic tests of insulation, mechanics, grounding, noise before end July
I.e. 2 × 14 RC-RC filters mounted 1/RC = 450 Hz
  Initial guess (to be corrected): R = 100 kΩ; C = 22 nF
  To be replaced with final values later

## Slide 8: Connectors
Found potentially interesting connectors from Farnell:
  http://www.farnell.com/datasheets/2916873.pdf
  Unit price (120 pins, small quant.): 53 € plug; 45 € pins; 26 € connector
  To be used for this prototype and replaced later