## Slide 1: Patch Panels
Luis Lopes, Orlando Cunha, Ricardo Gonçalo

## Slide 2: Status
Not much change since July
Holiday period and other activities
Tests done so far show necessary performance
Would like to better understand high-frequency response (see below)
Now working on:
Budget – assess assembly time and final cost
Optimizing design to improve cost and robustness
Collating information for SPR

## Slide 3: Prototype tests
RC–RC filter: 10 kΩ x 33 nF or 47 nF
Note R and C not final – must be defined together with sensors and tested together
Assuming 3 mA maximum current means:
60 V voltage drop
180 mW max. dissipation per channel
I.e. 5 W / 24-channel box
Ideal response:
fc = 338 Hz (33 nF) or 482 Hz (47 nF)
-40 dB / decade
Not quite what we see, but not far
Later tried same test inside metal box
Chart: dB vs log10(f)
| 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.397940008672037 | 3.69897000433602 | 3.8750612633917 | 4.0
dB | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206

## Slide 4: More tests
Measurements both with direct coupling (no High Voltage) and under HV bias from 0 V to 1000 V - injected signal through decoupling capacitor
Chart: 
| 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.397940008672037 | 3.69897000433602 | 3.8750612633917 | 4.0
dB (0V) | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206
dB (1 kV) | -33.4324 | -33.8501 | -34.6331 | -40.9151 | -49.1186 | -53.9794 | -57.7211 | -73.9794 | -75.563

## Slide 5: Current questions
Response improves with shielding (Faraday cage )
Closer to -40 dB / decade
Response flat above 10 kHz
Can investigate further
Or is this good enough?
Still to check:
Leak current under HV bias – waiting for precision HV module to be free, to ease measurement
Final tests must be done with HGTD HV source prototype
Chart: 
| 0.0 | 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.176091259055681 | 3.30102999566398 | 3.397940008672037 | 3.477121254719662 | 3.69897000433602 | 3.8750612633917 | 4.0 | 5.0 | 5.698970004336018 | 6.0
Shielding; direct; 33 nF | 0 | -0.33199 | -2.4988 | -7.2803 | -13.4324 | -18.0444 | -21.5403 | -27.5869 | -32.0412 | -36.1934 | -38.2373 | -46.4661 | -56.4782 | -58.0618 | -58.0618 | -58.0618 | -58.0618 | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
Shielding; direct; 47 nF | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
No shielding; direct; 33 nF | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206 | -46.0206 | -46.0206 | -46.0206

## Slide 6: Optimising design
Also trying an alternative design to:
Ease assembly: reduces production time and manufacture errors
Improve robustness: assess robustness of routing cables / soldering
Lower cost:
  Especially by reducing length of cable for HV routing
  Trying routing in 4-layer PCB

## Slide 7: Conclusions... so far
Initial prototype was very useful to gain confidence in design and performance
Some work still to be done, but seems in track
Now aim to improve plans with a view on production
Must define:
Final R and C values – together with sensor development
Final connectors – together with infrastructure
Would be very usefil to test together with prototype HV source
Prepare for SPR in October

## Slide 8
Thanks!

## Slide 9
Backup

## Slide 10: Connectors
Found potentially interesting connectors from Farnell:
  http://www.farnell.com/datasheets/2916873.pdf
  Unit price (120 pins, small quant.): 53 € plug; 45 € pins; 26 € connector
  To be used for this prototype and replaced later
REF:516-120-000-101 REF:516-056-000-301 REF:516-120-000-402 REF:516-056-000-402 REF:516-230-512 REF:516 230-556

## Slide 11: Measurements
Difficult to measure low-frequency behaviour with our current setup due to output capacitor in waveform generator

## Slide 12: Status of development
Preparing to build initial “Prototype 0”
Will produce 2 equipped boards for basic tests of insulation, mechanics, grounding, noise before end July
I.e. 2 × 14 RC-RC filters mounted 1/RC = 450 Hz
  Initial guess (to be corrected): R = 100 kΩ; C = 22 nF
  To be replaced with final values later

## Slide 13: Filter module
Initial idea: two PCBs per module with filters

## Slide 14: Modular box
Dimensions: 360 x 195 x 104 mm3 Weight: 7.5 kg (final around 10 kg)
56 wires in (28 pairs)
For insulation: male pins on USA15 side; female plugs on sensor side

## Slide 15: PCB with filters
14 RC-RC filters per PCB – 28 per module / Wire routing from connector to filter
Patching options:
56 wires in (28 pairs) – 56 wires out (28 pairs)
48 wires in (24 pairs) – 56 wires out (28 pairs)

## Slide 16: HGTD Involvement
Producing HV patch panels with CERN group:
16 patch panel boxes located around the calorimeter perimeter
Routing of High Voltage to HGTD detector and filtering AC noise out
Presented in Electronics meetings
Team: 1 academic, 2 engineers
Looking for new projects to get involved with in HGTD
Notes: Possibilities: TDAQ and DCS