## Slide 1: HGTD HV Patch Panels Status
Luis Lopes, Orlando Cunha, Ricardo Gonçalo

## Slide 2: Patch Panel Filter Design For PDR
HV routing through fixed wire connections between input long cables from USA15 and short cables to detector modules
2nd order RC-RC low-pass filter to suppress AC noise
  Up to -900 V with, no significant leakage, supply currents up to 3 mA per channel
  Decoupling capacitors to suppress common-mode noise (C3, C4)

## Slide 3: Patch Panel Filter Design For PDR
Differential HV channels, insulated from the patch panel unit
  Module aluminium boxes act as Faraday cage, electrically connected to the Tilecal surface
  HGTD earth extends through cable sleeve to filter board backplanes
  HGTD/Filter earth insulated from module earth (=Tilecal earth) to avoid ground loops

## Slide 4: PDR Discussion and Updates
HV PDR meeting on 29 August: https://indico.cern.ch/event/1190013/
Questions raised by Vincent Bobillier on grounding scheme and best way to suppress noise
  Suggested a discussion with Georges Blanchot, electronics engineer at CERN
Proposal for changed design in next page

## Slide 5: Proposed Changes
Use filter module boxes as continuation of vessel Faraday cage
  Also DC connecttion of filter boards backplane to cage
DC connection of Faraday cage to local TileCal earth
  DC current not as bad as HF AC noise
Move common-mode filter capacitors to filter input instead of output
  Filter common mode current at input

## Slide 6: Prototype tests and quality control
Planned tests:
  Connectivity of components and filter performance tested by measuring the filter response as function of frequency and load
  Leakage current
  Insulation between internal and external ground.
  Cross talk between channels
  Temperature under load
  Long term reliability including enhanced aging by temperature cycling in a climate chamber
  Radiation and magnetic field tolerances
  NEW: test with and without DC ground
For production:
  Based on prototype results will establish set of quality control benchmarks to be done in production and upon delivery

## Slide 7
Thanks!

## Slide 8: HGTD HV Patch Panels
Each of the 8032 HGTD modules will need a bias voltage between -300 V and -900 V, adjusted individually
Electronic noise induced in the DC bias voltage at the power supply or in the cables between USA15 and the detector must be filtered out.
Filter modules (EC-PP) will be installed on the end-cap calorimeter surfaces – filter noise and allow HV channel routing

## Slide 9: Patch Panel design parameters
Materials to withstand radiation and magnetic field:
  TID 15.0 Gy and 1 MeV neq fluence 1.0 × 1012 cm−2
  Magnetic field up to 0.5 Tesla
  Avoid easily activated and magnetic materials
  Avoid extensive use of dielectrics
Mechanical stability and ease of access during shutdowns
  Robust connectors
  Fixation to Tilecal and cable strain relief staves – to be studied together with Technical Coordination
Space constraints
  Around 20cm free in radial direction
  Number of wires should present good match to cables from HV supplies

## Slide 10: Patch Panel Units Design
A modular design is proposed for the patch panels
Individual modules are aluminium boxes containing two filter boards and connectors
  Provide mechanical support and insulate each pair of boards within separate Faraday cage
  Easy to construct, handle and access for maintenance
  14 RC-RC low-pass filters in each filter board
  Means one 56-wire cable connected to each module: = 28 HV channels = 14 channels x 2 boards
  Routing of individual HV channels through wires connecting cables to each filter board

## Slide 11
V
Shielded cable,
28 pairs
Individually floating channel HV supplies
Vessel wall
Shielded filter unit (28 channels)
Part of the Faraday cage by backplane of PCB connected to cable shields
Local earth USA15
Shield interrupted
at the supply.
Capacitor for ac coupling
Shield tied to backplane of filterboard via connector and cable
V
Shielded cable.
28 pairs
28-pin connector
Local earth PP-EC
Reference ground
CM filters

## Slide 12
V
Shielded cable,
28 pairs
Individually floating channel HV supplies
Vessel wall
Shielded filter unit (28 channels)
Part of the Faraday cage through connector shells
Local earth USA15
Shield interrupted
at the supply.
Capacitor for ac coupling
Shield tied to backplane of filterboard via connector and cable
V
Shielded cable.
28 pairs
28-pin connector
Local earth PP-EC
Reference ground
CM filters
Backplane of PCB connected to cable shields

## Slide 13: Initial (pre-)prototype tests
RC–RC filter: 10 kΩ x 33 nF or 47 nF
Note R and C not final – must be defined together with sensors and tested together
Assuming 3 mA maximum current means:
60 V voltage drop
180 mW max. dissipation per channel
I.e. 5 W / 24-channel box
Ideal response:
fc = 338 Hz (33 nF) or 482 Hz (47 nF)
-40 dB / decade
Achieved this when tested inside shielding box
Chart: dB vs log10(f)
| 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.397940008672037 | 3.69897000433602 | 3.8750612633917 | 4.0
dB | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206
Chart: 
| 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.397940008672037 | 3.69897000433602 | 3.8750612633917 | 4.0
dB (0V) | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206
dB (1 kV) | -33.4324 | -33.8501 | -34.6331 | -40.9151 | -49.1186 | -53.9794 | -57.7211 | -73.9794 | -75.563

## Slide 14: Prototype tests
Response improves with shielding (Faraday cage )
Closer to -40 dB / decade
Response flat above 10 kHz
Other tests foreseen:
Leak current under HV bias – waiting for precision HV module to be free, to ease measurement
Final tests must be done with HGTD HV source prototype
Chart: 
| 0.0 | 1.0 | 2.0 | 2.397940008672037 | 2.69897000433602 | 2.8750612633917 | 3.0 | 3.176091259055681 | 3.301029995663979 | 3.397940008672037 | 3.477121254719662 | 3.69897000433602 | 3.8750612633917 | 4.0 | 5.0 | 5.698970004336013 | 6.0
Shielding; direct; 33 nF | 0 | -0.33199 | -2.4988 | -7.2803 | -13.4324 | -18.0444 | -21.5403 | -27.5869 | -32.0412 | -36.1934 | -38.2373 | -46.4661 | -56.4782 | -58.0618 | -58.0618 | -58.0618 | -58.0618 | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
Shielding; direct; 47 nF | 0 | -0.67717 | -3.098 | -7.9588 | -13.7968 | -17.8898 | -21.6709 | -27.4322 | -32.9563 | -36.4782 | -38.9769 | -47.4322 | -55.1392 | -66.0206 | -66.0206 | -66.0206 | -66.0206
No shielding; direct; 33 nF | -2.1026 | -2.2702 | -7.4322 | -13.4324 | -18.4891 | -22.4988 | -32.9563 | -39.1721 | -43.7417 | -46.0206 | -46.0206 | -46.0206 | -46.0206

## Slide 15: Response curve
Response after adding common-mode decoupling capacitors

## Slide 16: Optimising design
Also tried an alternative design to:
Ease assembly: reduces production time and manufacture errors
Improve robustness: assess robustness of routing cables / soldering
Add decoupling capacitors against common-mode noise in each channel
Lower cost:
  Especially by reducing length of cable for HV routing
  Trying routing in 4-layer PCB

## Slide 17: Connectors
Found potentially interesting connectors from Farnell:
  http://www.farnell.com/datasheets/2916873.pdf
  Unit price (120 pins, small quant.): 53 € plug; 45 € pins; 26 € connector
  To be used for this prototype and replaced later
REF:516-120-000-101 REF:516-056-000-301 REF:516-120-000-402 REF:516-056-000-402 REF:516-230-512 REF:516 230-556

## Slide 18: Measurements
Difficult to measure low-frequency behaviour with our current setup due to output capacitor in waveform generator